## Slide 1: CDU UHF Screens

## Slide 2
CDU: UHF Main Screen
S 225.00
A 230.00 T
SQ
PROG
VOL 08
FRQ/CH
TST
MN/BOTH
Displays and Selects Frequency/ Channel (4)
I KHz Test Transmission On /OFF (3)
Select: Main or Both (5)
Display “T” when PTT/TST is pressed or MN or GD when Main or Guard is received (2&5)
Standby Frequency
Active or Tuned Frequency
Squelch ON/OFF (See Note 6)
Channel Program Mode Selection (7)
Volume display (See Note 1)
There are 21 volume level (0 to 20) without roll-over.
“T” is displayed when UHF radio is transmitting. (PPT or TST pressed). “T” is displayed when the ASCII “1” is sent from interface unit to RCP. See note 7 for MN/GD display function.
1.0 KHz audio tone is transmitted for 5 Sec when TST is pressed. If PTT is pressed during TST transmission TST is inhibited.
Pressing FRQ/CH soft button will scroll through displaying Main Frequency (FRQ) and Channel No(CH). The selection is highlighted.
MN/BOTH function is for receiver selection. The soft button select either MN or MN/BOTH. In Main (MN)mode the transmitting and receiving is on the displayed channel. In BOTH receiver scan on both MN and GD and locks to the either frequency. Locked frequency annunciator ( MN or GD) is displayed at the same location as “T”. Transmission in this mode is on MN frequency
Squelch is switch on or off by pressing “SQ” soft button. SQ is highlighted when selected.
Pressing the “PROG” soft button, displays the channel programming screen (shown in the next slide). In this mode a tuned frequency can be assigned to a selected channel.

## Slide 3
Delete Frequency of the Selected Channel (4)
CDU: UHF Program Screen
225.00
EXIT
CH1
Press button to select respective channel (1)
Selected Channel Frequency displayed (2)
Save and Exit to main page (3)
CH2
CH4
CH3
DELETE
Select channel to program by press respective soft key. The selected channel will be highlighted. By default CH 1 is highlighted. Only one channel can be selected at a time. A total of 20 Channels are available on the UHF RT
The selected channel frequency is displayed. The frequency can be edited by pressing the corresponding soft button to edit the frequency and keying in the new valve. Use the number pad to enter frequency, the back button to delete on digit at a time and the OK button to save the frequency. And OK again to make it the standby frequency.
To save the edited frequency and exit to main screen press “EXIT” soft key. To return to main page in the case of the delete or no change press “EXIT”.
To delete the frequency for the selected channel press the “DELETE” soft key. When deleted, “EMPTY” is displayed in place of frequency.
To scroll channel pages use the NEXT and BACK buttons on the keypad.. There are a total of 20 channels with 4 channels per page.
The “EMPTY” channels are inhibited.
BACK
NEXT