## Slide 1: CDU screens for VHF

## Slide 2: NAV COM CDU Screens
NAV
ADF
TACAN
M/B
HOME
BACK
HOME
OK
SWAP
Home screen at power up
Press soft button to select (e.g VHF soft button to select VHF radio).
A red text indicate that selection is not available (Not powered up or not functional or not connected)
Soft Buttons
Function Buttons
Soft Buttons
PREV
NEXT
HF
VHF
UHF
demo testing

## Slide 3: NAV COM CDU Screens VHF Selected
VHF
BACK
HOME
OK
SWAP
Active frequency is shown with prefix “A” and standby frequency is shown with prefix “S”
Press the swap button to swap active frequency with standby frequency.
To change the standby frequency select the “S xxx.xx” using soft button and change frequency using the
number pad. Use Back button to edit and OK to confirm.
Pre-set frequencies are stored as P 1----P 8. P1…. P4 are shown on page 1. Press “Next” button to see page 2 with P5….P8. Press “Back” to go back to page 1.
Press “Px” soft button to selected the pre-set frequency. Next press “Ok” to copy Px frequency as standby frequency.
PREV
NEXT
A 118.25
S 110.50
PROG
P 1
P 2
P 3
P 4
Pre programmed frequency selection soft keys

## Slide 4: NAV COM CDU Screens VHF Selected
NAV
BACK
HOME
OK
SWAP
To program P1…. P8. Select the location e.g P1 press “PROG”. The program page will be shown.
Using the key pad enter the frequency. Use “BACK” to edit and “OK” to store the new P1 frequency.
Upon pressing “OK” the program page will be replace with the last page ( NAV page).
PREV
NEXT
A 118.00
S 110.10
PROG
P1 110.250