## Slide 1: CDU Screen for HF Radio

## Slide 2: UI Rules
The CDU is designed for both Nav and COM. Using one of the switches on the motherboard the CDU can be configured as either Nav CDU or COM CDU.
“Black” text means that the radio (Nav or Com) is connected and available.
“Red” text means that the radio (Nav or Com) is not available.
Whenever a soft button is pressed (selected ) the text associated with it is highlighted.
Once the action relating to the highlighted button is executed the highlight box around the text is removed.
In case a selection is highlighted and not executed with in 45 sec the selection will revert back to the previous value. This will be applicable on all soft buttons. As an example if “STBY” (standby frequency) is selected and not swapped then it will revert back to the previous standby frequency.
The “NEXT” button and the “BACK” are used for scrolling through the Pre-programmed location pages. In most cases there will be only two pages.
Back button will also be used to move the cursor back when entering values from the key pad. e.g frequency, channel etc.
“OK” button is to be used confirm/enter/execute. For example after entering a standby frequency “Ok” will be pressed to confirm and execute.

## Slide 3: NAV COM CDU Screens
NAV
ADF
TACAN
MAIN
BACK
HOME
OK
SWAP
Main screen at power up
Press soft button to select (e.g VHF soft button to select VHF radio).
A red text indicate that selection is not available (Not powered up or not functional or not connected)
Soft Buttons
Function Buttons
Soft Buttons
PREV
NEXT
HF
VHF
UHF

## Slide 4: NAV COM CDU Screens HF Selected
HF
BACK
HOME
OK
SWAP
Active channel/frequency is shown with prefix “A” and standby channel/frequency is shown with prefix “S”
Press the “SWAP” button to swap active channel/frequency with standby channel/frequency.
To change the standby channel/frequency select the “S xxx.xx” using soft button and change channel/frequency using the number pad. Use “BACK” button to edit and “OK” to confirm.
Pre-set channel/frequencies are stored as P 1----P 8. P1…. P4 are shown on page 1. Press “Next” button to see page 2 with P5….P8. Press “Back” to go back to page 1.
Press “Px” soft button to selected the pre-set channel/frequency. The “Px” will be highlighted. Next press “Ok” to copy Px channel/frequency as standby channel/frequency.
PREV
NEXT
A 5100.0
S 4800.0
PROG
P 1
P 2
P 3
P 4
Pre programmed frequency selection soft keys
CH
FREQ

## Slide 5: NAV COM CDU Screens HF Selected
HF
BACK
HOME
OK
SWAP
To program P1…. P8. Select the location e.g P1 ( P1 will be highlighted) press “PROG”. The program page will be shown.
Using the key pad enter the channel/frequency. Use “BACK” to edit and “OK” to store the new P1 cannel/ frequency.
Upon pressing “OK” the program page will be replaced with the last page ( HF page).
PREV
NEXT
A 5100.00
S 4800.0
PROG
P1 4750.0
CH
FREQ
PROG
P 1
P 2
P 3
P 4