## Slide 1: CDU Screen for Nav Radio

## Slide 2: NAV COM CDU Screens
NAV
ADF
TACAN
M/B
HOME
BACK
HOME
OK
SWAP
Home screen at power up
Press soft button to select (e.g NAV soft button to select Nav radio).
A red text indicate that selection is not available (Not powered up or not functional or not connected)
The HOME button can be pressed at any time to revert back to the home page
Soft Buttons
Function Buttons
Soft Buttons
PREV
NEXT
HF
VHF
UHF

## Slide 3: NAV COM CDU Screens Nav Selected
NAV
BACK
HOME
OK
SWAP
Active frequency is shown with prefix “A” and standby frequency is shown with prefix “S”. These prefixes are default and can not entered.
Press the SWAP button to swap active frequency “A xxx.xx with standby frequency S xxx.xx.
To change the standby frequency select the “S xxx.xx” using the corrosponding soft button. The standby frequency will be highlighted.
Change the standby frequency using the number pad.
Use BACK button to edit and OK to confirm and save . The new standby frequency is saved only when OK button is pressed. If the OK button is not pressed with in 30 sec then the standby frequency reverts to old value.
PREV
NEXT
A 118.00
S 110.10
PROG
P 1
P 2
P 3
P 4
VOL
Pre programmed frequency selection soft keys

## Slide 4: NAV COM CDU Screens Nav Selected
NAV
BACK
HOME
OK
SWAP
Pre-set frequencies are stored at locations P 1 to P 8. Location P to P4 are shown on page 1, and locations P5 to P8 are shown on page to. Press “Next” button to see page 2. Press BACK to go back to page 1.
Press “Px” soft button to selected the pre-set frequency. The frequency valve is displayed at the bottom of the screen. Next press “Ok” to copy Px frequency as standby frequency.
PREV
NEXT
S 110.10
PROG
P1 120.250
A 118.00
VOL
PROG
P 1
P 2
P 3
P 4

## Slide 5: NAV COM CDU Screens Nav Selected
NAV
BACK
HOME
OK
SWAP
To program a pre-set location. Select the location e.g P4. Frequency value stored in “P4” for will be displayed at the bottom of the screen. If location P4 does not have any frequency stored than only “P4” will be displayed
Next Press the soft button “PROG”. The program page will be shown with the caption “PROG” shown above the P4 frequency, and the frequency value will be highlighted.
Using the key pad enter the frequency. Use “BACK” to edit and “OK” to store the new P4 frequency.
Upon pressing “OK” the program page will be replace with the last page ( NAV page).
PREV
NEXT
S 120.250
PROG
P4 110.250
A 118.00
VOL
PROG
P 1
P 2
P 3
P 4

## Slide 6: NAV COM CDU Screens Nav Selected
NAV
BACK
HOME
OK
SWAP
To program P1…. P8. Select the location e.g P4. P4 frequency will be displayed at the bottom of the screen
Next Press the soft button “PROG”. The program page will be shown with the caption “PROG” shown above the P1 frequency.
Using the key pad enter the frequency. Use “BACK” to edit and “OK” to store the new P1 frequency.
Upon pressing “OK” the program page will be replace with the last page ( NAV page).
PREV
NEXT
S 120.250
PROG
P4 110.250
A 118.00
P 1
P 2
P 3
P 4
VOL
PROG

## Slide 7: NAV COM CDU Screens Nav Selected
NAV
BACK
HOME
OK
SWAP
PREV
NEXT
A 118.00
S 110.10
PROG
P 1
P 2
P 3
P 4
VOL