## Slide 1: CDU Screen for Tacan

## Slide 2: NAV COM CDU Screens
NAV
ADF
TACAN
M/B
HOME
BACK
HOME
OK
SWAP
Home screen at power up
Press soft button to select (e.g Tacan soft button to select Tacan radio).
A red text indicate that selection is not available (Not powered up or not functional or not connected)
Soft Buttons
Function Buttons
Soft Buttons
PREV
NEXT
HF
VHF
UHF

## Slide 3: NAV COM CDU Screens Tacan Selected
TACAN
BACK
HOME
OK
SWAP
Active channel is shown with prefix “A” and standby channel is shown with prefix “S”
Press the swap button to swap active channel with standby channel.
To change the standby channel select the “S xxx.” using soft button and change channel using the
number pad. Use Back button to edit and OK to confirm.
Pre-set channels are stored as P 1----P 8. P1…. P4 are shown on page 1. Press “Next” button to see page 2 with P5….P8. Press “Back” to go back to page 1.
Press “Px” soft button to selected the pre-set channel. Next press “Ok” to copy Px channel as standby channel.
PREV
NEXT
A 83Y
S 22Y
PROG
P 1
P 2
P 3
P 4
Pre programmed frequency selection soft keys
MODE

## Slide 4: NAV COM CDU Screens Tacan Selected
NAV
BACK
HOME
OK
SWAP
To program P1…. P8. Select the location e.g P1 press “PROG”. The program page will be shown.
Using the key pad enter the channel. Use “BACK” to edit and “OK” to store the new P1 channel.
Upon pressing “OK” the program page will be replace with the last page ( NAV page).
PREV
NEXT
A 83X
S 22Y
PROG
P1 19X